## Slide 1
How the RISC-V Debugger Works
A Plain-English Visual Guide to the On-Chip Debug Architecture
No Fluff • Only Active Signals • Core Halt/Resume • Accelerator Access • All 8 Features

## Slide 2
The Big Picture: How Everything Connects
Only 4 key blocks inside the chip — simple and clean
HOST PC
Your Laptop / Terminal
• Runs PuTTY or Python CLI • Sends text commands • Displays read data Uses normal USB cable!
UARTSin / UARTSout
DEBUGGER
riscv_debugger_top
• Uses Uncore 16550 UART • Direct internal streaming • Translates ADP text to AHB • Holds Pause Button: 'core_halt_o' • Controls AHB Master 1
PAUSE
BUS M1
RISC-V CPU
wallypipelinedcore
• Runs your firmware • Freezes when PAUSE=1 • Master 0 on AHB Bus
AHB MUX
Traffic Cop (ahb_mux)
• Decides who talks • CPU wins when running • Debugger wins when paused
BUS
CHIP MEMORY
Uncore & Accelerators
[ACCELERATOR] • 0x30000000 space • Product = 42 • Large 16MB window [MAIN RAM] • Program variables [PERIPHERALS] • 16550 UART (Console+Debug), Timers, GPIO

## Slide 3
Exact Active Wires & Signals
We trimmed all unused signals — only these real wires exist in the code
1. External Serial & Debug Streams
• UARTSin / UARTSout (1-bit):
Shared physical pins into Uncore 16550 UART
• dbg_uart_rx_* (Stream):
Direct byte stream from Uncore UART to ADP
• dbg_uart_tx_* (Stream):
Response stream from ADP to Uncore UART
• Zero Duplication:
Reuses existing UART; only 2 pins for entire SoC!
2. Core Freeze & Reset
• core_halt_o (1-bit):
Connected to 'ExternalStall' in hazard.sv
• Halt State:
1 = All 5 CPU stages freeze in place
• Run State:
0 = CPU continues normal execution
• core_reset_o (1-bit):
Optional board/core reset wire
3. Debugger AHB Master (M1)
• DEBUG_HADDR[31:0]:
Target address to read or write
• DEBUG_HWDATA[31:0]:
Write data from host to memory
• DEBUG_HRDATA[31:0]:
Read data returning from memory
• DEBUG_HTRANS[1:0]:
2'b00 = IDLE, 2'b10 = Active transfer
• DEBUG_HWRITE:
1 = Write, 0 = Read
• DEBUG_HREADY:
1 = Slave finished transfer
4. AHB Mux Output (S)
• S_HADDR[31:0]:
Selected address sent to memory/accelerator
• S_HWDATA[31:0]:
Selected write data
• S_HRDATA[31:0]:
Shared read data routed back to active master
• grant_addr:
Internal bit: 0=CPU has bus, 1=Debugger has bus

## Slide 4
The AHB Mux: Who Gets to Talk to Memory?
A smart arbiter that eliminates bus contention completely
SCENARIO A: CPU IS RUNNING (core_halt = 0)
Your application code is actively executing
▶ Who has priority?
THE CPU WINS ALWAYS
▶ Why?
Your real-time software, interrupts, and motor/sensor control are never delayed by the debugger.
▶ Can Debugger still read?
YES! (Cycle Stealing)
▶ How cycle-stealing works:
Whenever CPU is computing internal math or fetching from cache, the bus is IDLE. The MUX instantly lets the debugger read/write memory during that free cycle!
▶ Collision behavior:
If both want the bus at the exact same cycle, CPU goes first; debugger waits 1 cycle.
SCENARIO B: CPU IS PAUSED (core_halt = 1)
You sent command 'C 0202' to pause the core
▶ Who has priority?
THE DEBUGGER WINS 100%
▶ Why?
The CPU pipeline is completely frozen in place. It will not make any bus requests.
▶ What can you do?
Total control of the chip!
▶ Inspection benefits:
You can inspect static accelerator output, modify registers, inspect variables, or load new firmware without the CPU changing anything under your feet.
▶ Zero Contention:
Bus is 100% dedicated to your serial commands.

## Slide 5
All 8 Features of the Debugger
More than just a reader — a full diagnostic and hardware control suite
1. Core Freeze & Thaw
Pause CPU mid-instruction with 'C 0202'; unpause with 'C 0102'. No crash, no reset.
2. Live Memory Peek
Read any RAM or peripheral address on the fly without stopping the CPU ('R' command).
3. Memory Poke (Write)
Change parameters, tweak accelerator inputs, or inject values into memory ('W' command).
4. Dedicated Accelerator Window
Direct access to the 16 MB accelerator window (0x30000000) for dummy or big accelerators.
5. Hardware Auto-Polling ('P')
Hardware polls a 'Busy/Done' flag at 50 MHz and only replies when the calculation finishes.
6. High-Speed Memory Fill ('F')
Zeroes out or patterns entire memory buffers at hardware bus speed in 1 command.
7. Binary Firmware Upload ('U')
Stream raw compiled binary code directly into RAM for instant testing without flashing ROM.
8. Bus Error Detection ('!')
If you touch an invalid address, it alerts with '!' instead of hanging the entire chip.

## Slide 6
Action Flow: Freezing & Resuming the CPU
Simple 3-step timeline of what happens inside the chip
Step 1: You Type 'C 0202'
You send 6 text characters over serial terminal. Uncore 16550 UART receives bytes via UARTSin and streams them to the ADP engine.
Step 2: Hardware Pause Signal
socdebug_adp_control sets GPO8 bit 1. core_halt_o immediately goes HIGH (1) into hazard unit.
Step 3: All 5 Stages Freeze
hazard.sv sets StallW = StallM = StallE = StallD = StallF = 1. Pipeline freezes like a paused video game!
Step 4: You Type 'C 0102' (Resume)
core_halt_o goes LOW (0). Pipeline unfreezes and CPU seamlessly continues its work!

## Slide 7
Action Flow: Reading the Accelerator Register
How reading address 0x30000008 fetches the product (42)
Step 1: Set Target Address
You send: 'A 30000008\n' Debugger stores 0x30000008 into its address register and replies 'A 0x30000008'.
Step 2: Send Read Command
You send: 'R\n' Debugger generates AHB Master cycle: HADDR = 0x30000008 HTRANS = NONSEQ HWRITE = 0 (Read)
Step 3: Mux Routes to Slave
ahb_mux activates accelerator chip-select (HSELEXT). multiplier_ahb decodes offset 0x08 and drives product (42) onto HRDATA.
Step 4: Result Sent to PC
Debugger formats the result into text: 'R 0x0000002A ]' and streams it through the Uncore UART out over UARTSout to your PC terminal: 42 (0x2A)!

## Slide 8
Command Cheatsheet at a Glance
Only 6 simple commands cover 99% of your debugging needs
C 0202
PAUSE CPU — Freezes CPU pipeline in place via ExternalStall
C 0102
RESUME CPU — Unfreezes CPU pipeline to continue running normal code
A <hex_addr>
SET ADDRESS — Sets memory pointer (e.g. 'A 30000008' for accelerator)
R
READ WORD — Reads 32-bit value at address pointer and prints in hex
W <hex_val>
WRITE WORD — Writes 32-bit value to address pointer (e.g. 'W 00000007')
P <timeout>
AUTO-POLL — Waits for accelerator calculation to finish without CPU help